Indicators adapted for 4.50 MW Akkihebbal

Mini Hydel Scheme in Karnataka, India

Version 1.0, October 2014

Content

- Identifying the Project

- Project Description

- Indicators to be excluded

- Identifying the Project

Project name: 4.50 MW Akkihebbal Mini Hydel Scheme in Karnataka, India

Person responsible for reviewing or adapting the indicators (name and contact): Srinidhi S. Rao; e-mail: srinidhi@emergent-ventures.com

Version/Date of indicator to be reviewed or adapted: Indicators for Hydroelectric Power Plants, Version 4.1 – June, 2011

Result: Indicators adapted for 4.50 MW Akkihebbal Mini Hydel Scheme in Karnataka, India

- Project Description

The project activity comprises generation of electricity using renewable energy based on hydro power and its supply to the Southern grid. It hence displaces the electricity which would have otherwise been generated from the power plants connected to the grid. The mini hydro project has been set up in the state of Karnataka in India across the river, Hemavathy, a tributary of the east flowing river, Cauvery. The project activity has an installed capacity of 4.50 MW to generate about 13 MU annually. The hydro power project is based on the run-of-river (ROR) scheme.

The project activity is a mini hydel project which will supply power through Southern Grid. The purpose of the project activity is to generate electricity using renewable hydro energy and to use to meet the energy demands of the region. In the absence of the project activity, equivalent power would have been generated based on the fossil fuels resulting in greenhouse gas (GHG) emissions into the atmosphere. Thermal power plants are the greatest contributor (65% in 2005-06) of exported power to the Southern grid.

Water Approaching the Plant, diverted by the weir:

Water from the Forebay moving towards the Generation Room (Turbines):

Turbines in the Generation room and the Control Room:

By utilizing the flow of the river, the project activity is:

- Utilizing the untapped mechanical energy resource, this was otherwise being wasted.

- Contributing to the power requirements of state of Karnataka thereby positively contributing to growth of the state;

- Conserving the environment and its natural resources through use of renewable energy;

- Also reducing the need for transportation of the fuels;

- Protecting the environment from degradation due to deforestation (on using wood based fuels) or pollution (due to use of fossil fuels for energy or the transportation of fuels);

- Reducing GHG emissions.

Project technologies, products, services and the expected level of activity:

This project has an installed capacity of 4.5 MW and will be generating ~ 13 MU of average annual net electricity. The above energy potential is harnessed by installing 2 units if 2.25 MW units with the combined design discharge of 77.38 cumecs (with 15% overload to a maximum total of 96 cumecs). The project activity’s inflow is to some extent dependent upon regulated release from the Hemavathy Dam, which includes a higher flow during non monsoon period due to storage of the dam. In addition inflow is also from independent catchment area also. The total catchment area of the river up to the proposed activity is about 4900 sq.km. The total design flood for the weirs is 6757 cumecs.

Technical specifications of the project activity:

| PARAMETER | VALUES |
| --- | --- |
| Hydrology |
| Catchment Area | 4900 sq. km |
| Independent Catchment Area | 2082 sq. km |
| Design Discharge | 6757 cumecs |
| Main Weir |
| Crest Level | El 766 m |
| Length and Height | 308m and 2m Average |
| Left Limb Weir |
| Crest Level | El 766 m |
| Length and Height | 296m and 2m average |
| Approach Channel |
| Length | 50m |
| Bed Width | 30m |
| Bed Level near Intake | El 762.40 |
| Forebay |
| Size | 63m X 24m |
| Tail Channel |
| Length | 92 m |
| Power House |
| Design Head | 6.94m |
| Type of Unit | S-Type Full Kaplan |
| Design Discharge for two units | 77.38 cumecs |
| Installed Capacity | 2 X 2.25 MW= 4.5 MW |
| Average Annual Net Generation | MU |

- Indicators to be excluded

| Name of the indicator | Justification for excluding the indicator |
| --- | --- |
| Reservoir and Marginal Areas Management | This indicator is applicable for reservoir type of projects whereas the present project activity is a run of river. Further the marginal area surrounding the project activity has no bearing on the project; hence this indicator has been excluded. |
| APP and Legal Reserve | The project is situated a few kilometers away from Akkihebbal village of Krishnarajapet (Taluk), Mandya (district), in the state of Karnataka, India. There is no APP and Legal Reserve area surrounding the project activity. Hence the indicator has been excluded. |

# Text boxes

RIVER FLOW

APPROACH CHANNEL

FOREBAY

TURBO-GENERATORS

ELECTRICITY

SUBSTATION

REGIONAL GRID